## Slide 1: On the Identification of Variances and Adaptive Kalman Filtering

## Slide 2: Kalman Filter Calculation:
A Kalman filter needs the exact knowledge of:
The process noise’s covariance matrix represented by Q
The measurement’s noise covariance matrix , represented by R

## Slide 3: Paper Assumptions:
The true value of these 2 matrix is unknown.
Inputs are random and stationary.
The results are first derived for discrete systems, and then extended to continuous ones.

## Slide 4: System Assumptions:
The system under consideration is time invariant.
It is completely controllable and observable.
Both the system and filter (whether they are optimal or suboptimal) area assumed to have reached steady-state conditions.

## Slide 5: Path to Solution:
A correlation test is given in order to check whether a particular Kalman filter is working optimally or not
In the case of suboptimal result a technique is given.
Using this technique an approximated normal, unbiased, and consistent estimates of Q and R are found
This technique only works for special cases where Q’s form is known and the number of its unknown elements is less than n*r. (n representing dimension of the state vector and r representing that of measurement vector.)
For other cases, the optimal steady-state gain represented by Kop is calculated iterative by an iterative procedure without identifying Q.

## Slide 6: Formulas for Defining System:
A MULTIVARIABLE LINEAR DISCRETE SYSTEM
xi is n*1 state vector
Φ is n*n nonsingular transition matrix
Γ is n*q constant input matrix.
zi is r*1 measurement vector.
H is r*n constant output matrix.

## Slide 7: Formulas for Defining System:
A MULTIVARIABLE LINEAR DISCRETE SYSTEM
Sequences ui with n*1 and vi with r*1 as their size, are uncorrelated Gaussian white noise sequences.
Initial state xo is normally distributed with:

## Slide 8: Formulas for Defining Filter:
Ko is a n*r matrix representing the steady-state Kalman filter gain.
Mo is the steady-state solution to the covariance equation of Kalman.
Qo and Ro are the initial states of Q and R

## Slide 9: Formulas for Defining Filter :
FILTERING EQUATIONS
is the estimate of xi+1 based on all the measurements up to i.

## Slide 10: Two Cases:
Case 1: Optimal Kalman Filter:
When Q = Q0 and R = R0. In these cases M0 is the covariance of the error in estimating the state.
Case 2: Suboptimal Kalman Filter:
The covariance of the error called M1 , is given by the following equation:

## Slide 11: Problem and Approaches:
THE TRUE VALUES OF Q AND R ARE UNKNOWN
Check whether the Kalman filter constructed using some estimations of Q and R are close to optimal or not.  Hypothesis Testing
Obtain unbiased and consistent estimates of Q and R.  Statistical Estimation
Adapt the Kalman filter at regular intervals using all the previous information  Adaptive Filtering

## Slide 12: Simulation Given Parameters:
 Nonsingular Transition Matrix
 Constant Input Matrix
 Constant Output Matrix
 Input Covariance Matrix
 Noise Covariance Matrix

## Slide 13: Initial Values:

## Slide 14: Optimality Test:
If the above values are given as initial values, then we are dealing with a suboptimal filter and as a result, we expect to see more than 5 percent of outside of 95% confidence interval.
In order to find, sequence of is simulated, and then the estimator of Ck meaning is calculated with . After that, is computed with

## Slide 15: Optimality Test Results:

## Slide 16: Formula for Calculating Estimators of Q and R:

## Slide 17: Results of Calculating Estimators of Q and R:

## Slide 18: Optimality of Filter:

## Slide 19: 10 Batch Data Results for R:

## Slide 20: 10 Batch Data Results for Q:

## Slide 21: Thank You.